Page 1 of 3

Material Safety Data Sheet

Name PETROLEUM JELLY, PN-011   MSDS clpcg

Company HDMCO HOLDING GROUP, INC.       FSC 6505

MF""1 Safety Information f!   6505 NUN: 00-133-8025 MSDS Date: 07/21/1997 MSDS Num: CLPCG

Product ID: PETROLEUM JELLY, PN-011 MFN: 01 Responsible Party

Cage: T0364

Name: HUMCO HOLDING GROUP, INC.

Address: 7400 ALUMAX DRIVE

City: TEXARKANA TX 75501

Info Phone Number: 903-831-7808

Emergency Phone Number: 800-424-9300

Chemtrec IND/Phone: (800)424-9300

Review Ind: Y

Published: Y

Contractor Summary

Cage: TO364

Name: HUMCO HOLDING GROUP, INC

Address: 7400 ALUMAX DRIVE

City: TEXARKANA TX 75501

Phone: 903-831-7808

Item Description Information

Item Name: PETROLATUM, WHITE, USP

Specification Number: NONE

Type/Grade/Class: NONE

Ur>J4- of Issue: CO

U,  ^ntainer Qty: 1

Type of Container: UNKNOWN

Ingredients

Cas: 8009-03-8

RTECS #: SE6780000

Name: PETROLEUM WHITE U.S. P.

Other REG Limits: NONE

OSHA PEL: 5MG/M3 OIL MIST TWA

ACGIH TLV: NONE

Health Hazards Data

Route Of Entry Inds - Inhalation: YES

Skin: NO

Ingestion: YES

Carcinogenicity Inds - NTP: NO

IARC: NO

OSHA: NO

Effects of Exposure: POTENTIAL HEALTH HAZARDS: SKIN: NON-IRRITATING. EYES: MAY BE SLIGHTLY IRRITATING TO THE EYES. INHALATION: OIL MIST CONCENTRATION OF 50 MG/M3 CAN CAUSE SHORTNESS OF BREATH, COUGHING OR WHEEZING. INGEST ION: INGESTION OF A LARGE DOES MAY HAVE A LAXATIVE EFFECT AND CAUSE CRAMPS AND DIARRHEA. RISK OF ASPIRATION.

Explanation Of Carcinogenicity: NO INGREDIENTS LISTED IN THIS SECTION.

Medical Cond Aggravated By Exposure: PRE-EXISTING EYE, SKIN AND RESPIRATORY DISORDERS AND ASTHMA.

First Aid- SKIN- IN CASE OF SKIN CONTACT REMOVE CONTAMINATED CLOTHING, WASH AFFECTED AREA WITH SOAP AND WATER. EYE: IN CASE OF EYE CONTACT, IMMEDIATELY ~T,USH EYES WITH PLENTY OF WATER, KEEPING EYELIDS WIDE OPEN.  INHALATION: IF

L MIST INHALED REMOVE PATIENT TO FRESH AIR. IF NOT BREATHING GIVE ARTIFICIAL RESPIRATION. IF BREATHING IS DIFFICULT, OXYGEN CAN BE GIVEN BY A QUALIFIED OPERATOR. INGESTION: IF SWALLO WED, DO NOT INDUCE VOMITING UNLESS ADVISED BY A PHYSICIAN DUE TO RISK OF ASPIRATION. GET PROMPT MEDICAL ATTENTION.

m

i ii<!/Pr/msHs/fnrdfieldhouse/PetroliumJelly.txt	7/10/2007

ndling and Disposal

ill Release Procedures: ALWAYS WEAR THE PROPER PERSONAL PROTECTIVE EQUIPMENT. ISOLATE THE SPILL AREA AND CONTAIN. ONLY TRAINED PERSONNEL FITTED WITH THE PROPER PERSONAL PROTECTIVE EQUIPMENT SHOULD BE ALLOWED TO ENTER THE SPI LL n~TE. COLLECT THE SPILL IN A WASTE CONTAINER FOR DISPOSAL. FLUSH THE SPILL

,A THOROUGHLY WITH WATER. SPILL CAN CAUSE VERY SLICK SURFACES! ste Disposal Methods: DISPOSE ACCORDING TO FEDERAL, STATE AND LOCAL REGULATIONS.

ndling And Storage Precautions: DO NOT STORE ABOVE 120F (49C) KEEP AWAY FROM SOURCES OF INGNITION AND OXIDIZING MATERIALS. ALWAYS USE IN A WELL VENTILATED AREA.

her Precautions: KEEP AWAY FROM CHILDREN! re and Explosion Hazard Information ash Point Method: COG ash Point: =204.4C, 400.F

tinguishing Media: SMALL FIRE: USE CARBON DIOXIDE OR DRY CHEMICAL. LARGE FIRE: USE ALCOHOL FOAM. NOTE: NORMAL FIRE FIGHTING FOAMS THAT ARE SUITABLE FOR GASOLINE OR HYDROCARBON (FIRE/EXPLOSION HAZARD.)

re Fighting Procedures: USE NIOSH-APPROVED SELF-CONTAINED BREATHING APPARATUS AND FULL PROTECTIVE EQUIPMENT (FP N). USE WATER TO KEEP FIRE EXPOSED TANKS AND CONTAINERS COOL. WATER OR FOAM MAY CAUSE FROTHING OF MOLTEN MATERIA L. DO NOT ENTER FIRE AREA WITHOUT PROPER PERSONAL PROTECTIVE EQUIPMENT TO INCLUDE A SELF-CONTAINED BREATHING APPARATUS.

usual Fire/Explosion Hazard: DENSE SMOKE MAY BE GENERATED WHEN BURNING. EXTINGUISHING MEDIA (CON'T): FIRES WILL BREAK DOWN AND WILL NOT EXTINGUISH FIRES. WATER SPRAY WILL REDUCE THE INTENSITY OF THE FLAMES, ntrol Measures

spiratory Protection: USE A NIOSH-APPROVED RESPIRATOR APPROPRIATE FOR THE EXPOSURE OF CONCERN (FP N). IF SURROUNDING ATMOSPHERE CONTAINS AN OIL MIST OF 50 MG/M3 OR GREATER THEN A FULL FACE AIR SUPPLIED RESPIRATOR IS RECOMM ENDED, ntilation: ALWAYS USE IN A WELL-VENTILATED AREA, -"active Gloves: IMPERVIOUS GLOVES FOR  PROLONGED OR HOT EXPOSURES (FP N).

Protection: ANSI APPROVED CHEMICAL SAFETY GOGGLES (FP N). (SUPP SFTY) her Protective Equipment: EYE WASH AND DELUGE SHOWER MEETING ANSI DESIGN CRITERIA (FP N). APRON AND SLIP RESISTANT WORK BOOTS IF CLEANING LARGE SPILLS.

>rk Hygienic Practices: FOLLOWING GENERALLY RECOGNIZED SAFETY PRACTICES AND SOUND WORK METHODS SHOULD BE USED WHEN HANDLING THIS PRODUCT IN LARGE OR SMALL QUANTITIES.

.pplemental .Safety and Health: EYE PROTECTION (CON'T) : NONE NEEDED WHEN USED IN JELLY FORM. IF IN LIQUID FORM USE CHEMICAL GOGGLES. lysical/Chemical Properties •iling Point: =343.3C, 650.F .por Pres: 1 MMHG @ 20C .por Density: 1 (AIR=1) >ec Gravity: 0.86 (H20=l) •aporation Rate ANDamp; Reference: NONE ilubility in Water: INSOLUBLE

ipearance and Odor: YELLOWISH, TRANSLUCENT JELLY.  ODOR: NONE, sactivity Data lability Indicator: YES

lability Condition To Avoid: NORMALLY STABLE.  KEEP AWAY FROM HEAT, SPARKS AND FLAME.

iterials To Avoid: AVOID STRONG OXIDIZING AGENTS.

izardous Decomposition Products: CARBON MONOXIDE, WTER VAPOR AND UNIDENTIFIED ORGANIC COMPOUNDS.

izardous Polymerization Indicator: NO >xicological Information -^cological Information: N/P.

ogical Information :ological: N/P. JDS Transport Information ransport Information: N/P. jgulatory Information

tp://web.srcc.cc.mi.us/Pr/msds/fordfieldhouse/PetroliumJelly.txt

Sara Title III Information: N/P.

Federal Regulatory Information: N/P.

State Regulatory Information: N/P.

Other Information

Otv - Information: NFPA: HEALTH - 0, FIRE - 1, REACTIVITY - 0. NATIONAL FIRE '.  ,TECTION ASSOCIATION (NFPA) LEGEND: 4=EXTREME, 3=SERIOUS, 2=MODERATE, 1=SLIGHT, 0=MINIMAL. PRODUCT USE: MOISTURIZER.

HAZCOM Label

Product ID: PETROLEUM JELLY, PN-011

Cage: T0364

Assigned IND: Y

Company Name: HUMCO HOLDING GROUP, INC

Street: 7400 ALUMAX DRIVE

City: TEXARKANA TX

Zipcode: 75501

Health Emergency Phone: 800-424-9300

Label Required IND: Y

Date Of Label Review: 10/24/2001

Status Code: A

Origination Code: F

Eye Protection IND: YES

Skin Protection IND: YES

Signal Word: WARNING

Respiratory Protection IND: YES

Health Hazard: Moderate

Contact Hazard: Slight

Fire Hazard: Slight

Reactivity Hazard: None

Hazard And Precautions: POTENTIAL HEALTH HAZARDS: ACUTE: SKIN: NON-IRRITATING. EYES: MAY BE SLIGHTLY IRRITATING TO THE EYES. INHALATION: OIL MIST CONCENTRATION OF 50 MG/M3 CAN CAUSE SHORTNESS OF BREATH, COUGHING OR T'"7EEZING.  INGESTION: INGESTION OF A LARGE DOES MAY HAVE A LAXATIVE EFFECT 1  J CAUSE CRAMPS AND DIARRHEA. RISK OF ASPIRATION. CHRONIC: NONE SPECIFIED BY MANUFACTURER (FP N).

Disclaimer

(provided with this information by the compiling agencies): This

information is formulated for use by elements of the Department of Defense. The United States of America in no manner whatsoever expressly or implied warrants, states, or intends said information to have any application, use or viability by or to any person or persons outside the Department of Defense nor any person or persons contracting with any instrumentality of the United States of America and disclaims all liability for such use. Any person utilizing this instruction who is not a military or civilian employee of the United States of America should seek competent professional advice to verify and assume responsibility for the suitability of this information to their particular situation regardless of similarity to a corresponding Department of Defense or other government situation.